## Slide 1: 快樂玩雲端之 Kingston IIoT分享
講者：Carl Yang

## Slide 2: Challenges
多樣化的資料來源
不一致的資料格式
網路通訊的難易度
龐大的資料量

## Slide 3
Azure IoT Hub

## Slide 4: Scale
Free:
  Only 1 per subscription
Basic:
  Device-to-cloud
Standard:
  Cloud-to-device
  IoT Edge
  Device Management
MQTT、AMQP
  Lightweight
(Ref: https://docs.microsoft.com/en-us/azure/iot-hub/iot-hub-scaling)

## Slide 5: Telemetry
Cache: 1~7 days
Unified format
Unstructured
Data Centralizing
相同事件、相同時間

## Slide 6: Consumer Group
Pulling data
Max. 20 consumer groups per IoT Hub
5 concurrent readers per group

## Slide 7: File Upload
Only Support Storage Container
Only Block blobs
10 concurrent keys in queue
  同時10台裝置上傳

## Slide 8: Query Explorer
Only in Standard Tier
Device Twins/Jobs
information
Help to manage devices

## Slide 9: Architecture

## Slide 10
Data Flow
Monitor
AuthN/AuthZ

## Slide 11: Data Flow

## Slide 12: Monitor

## Slide 13: Authentication

## Slide 14: Data

## Slide 15
要用資料做什麼?
分析、警示、統計?

## Slide 16: 分析 – 以O2為例

## Slide 17: 警示– 以O2為例

## Slide 18: 統計 – 以WIP為例

## Slide 19
資料從哪裡來?
Devices、OCR?
Machine Logs!

## Slide 20: Sources
Sources:
  Devices:
    Devices Support
    Weak Integration
  OCR:
    視覺辨識技術
  Machine Logs:
    Native Machine Software Support
    Stable

## Slide 21
資料如何處理?

## Slide 22: Various Data Structures
Principals:
  Keep useful data
  Re-organize structure
  Merge/Divide Values
  Use CSV for collecting

## Slide 23: Azure Cache for Redis
Shared
  Snapshot
Performance
  Cache in memory
Mem Usage
  maxmemory-policy
  LRU(less recently used)
https://docs.microsoft.com/en-us/azure/architecture/best-practices/caching?toc=/azure/redis-cache/toc.json

## Slide 24: Azure Cache for Redis
SSL:
  Port: 6380(default)
Non-SSL:
  Port: 6379

## Slide 25: Azure Cache for Redis
Shorten Key
  SHA 256 to generate key
  Fixed Length
Hash Keys/Fields/Values
  效能較好
  HMSET/HMGET、批量操作
Compression
  降低傳輸耗時
  降低MEM使用量
  壓縮前後、差13倍以上
Split to several parts

## Slide 26
資料往哪裡送?怎麼送?

## Slide 27: Principals for IoT Hub
256 KB per message
  Make data size closed to 256 KB in each request
4 KB per unit
  Reduce data size as possible, ex. \u0022
256 KB
256 KB
128 KB
IoT Hub
1
2
3

## Slide 28: Memory Queue
256 KB
256 KB
128 KB
IoT Hub
Latency
Time Series

## Slide 29: Application

## Slide 30: IoT Edge
最接近資料來源的機器
分散式計算
獨立運算能力
網路通訊能力

## Slide 31: IoT Devices or Edge?
政策
遠端裝置管理
雙向通訊
Device Client作業環境
Device Client的網路環境

## Slide 32: Win Services or Container?
Docker
  Memory Process，注意使用量。
  Windows環境下，盡可能不使用大量的Disk I/O處理。
Windows Services
  管理不易
  Debug資訊不充足
  系統整合性佳

## Slide 33: Cost

## Slide 34: Basic or Standard tier?
(Ref:https://azure.microsoft.com/zh-tw/pricing/details/iot-hub/)

## Slide 35: Azure IoT Hub Quota
Charge Unit: 4KB
Batch Daily Volume:
  Type1: 0.18 KB x 60s x 60m x 24H x 12 Lines = 186,624 KB
  Type2: 0.98 KB x 60/10s x 60m x 24H x 12 Lines = 101,606 KB
  Total: 288,230 / 4 KB = 72,057 Units
Real-time Daily Count:
  Type1: 60s x 60m x 24H x 12 Lines = 1,036,800 records
  Type2: 60/10s x 60m x 24H x 12 Lines = 1,036,80 records
  Total: 1,036,800 + 1,036,80 = 1,140,480 Units

## Slide 36
Contact:
  Carl_Yang@kingston.com.tw
PPT:
  https://github.com/carlyang920/knet2021.git

## Slide 37: Thanks for joining!
Notes: Thanks for joining us! Have a great conference!